## Slide 1: Efficient Hardware Implementation of AES
Introduction
To securely transmit data, cryptography is used. There are two types of cryptographic systems: Symmetric and Asymmetric.
Symmetric cypher algorithms use identical keys for the sender and the receiver.
Rijndael algorithm , which is a symmetric, block cryptosystem, was chosen as the Advanced Encryption Standard (AES) by the NIST on 2nd Oct 2000.
Hardware implementation provides greater speeds and higher reliability with large amount of data [1].
Advanced Encryption Standard
AES algorithm is very robust because of the different key lengths, which results in AES-128, AES-192 and AES-256 format encryption for a 128-bit (16 word) block data.
For this project, the implementation is using a key length of 128 bits.
The Key is expanded into 44-word key.
  Look Up Tables and ROM Implementation
Implementation utilizes LUTs (ROM) for the S-box SubBytes layer, multiplication in MixColumns layer [2].
This reduces the computation cost otherwise needed for matrix multiplication in Galois field GF(28).
This is a Moore FSM; the states depend on the internal enable.
This implementation represents only first round for the AES. FSM stays in a state until the calculation of the state is not finished.
References
[1] P. S. Abhijith, M. Srivastava, A. Mishra, M. Goswami, and B. R. Singh, "High performance hardware implementation of AES using minimal resources," pp. 338-343, 2013, doi: 10.1109/ISSP.2013.6526931.
[2] W. McLoone and J. V. McCanny, "Rijndael FPGA implementation utilizing look-up tables," vol. 34, pp. 349-360, 2001, doi: 10.1109/SIPS.2001.957363.
AES round description
SubBytes uses a LUT to substitute input 8-bits.
ShiftRows rotates the rows of the 16-byte block through a fixed pattern.
In the MixColumns layer multiplication of the block data is performed in Galois field GF(28).
Name: Sachleen S. Chani Mentor: Dr. Vijaypal Singh Rathor
Roll No. : 101506143
Department of
Electronics & Communication Engineering
AES Parameters
AES Round Functions
Galois Multiplication by 2 LUT
Verilog Implementation
Top Level block diagram
AES State diagram
Abstract
Hardware implementation of cryptographic algorithms is inherently more secure.
An effective way to implement the AES algorithm in FPGA is explored in this project.
Higher speeds and lesser area could be achieved by designing the SubBytes and MixColumns layers as a Look Up Tables (LUTs) and ROMs.